## Slide 1: Assignment 2-B TurtleBot3 Open-Loop Control
GROUP 1
Chinmay Vilas Samak
Tanmay Vilas Samak
GitHub Repository

## Slide 2: Overview
Circle
  Move robot in circle with specified constant twist command
  Radius of circle determined by ratio of linear and angular velocities (kinematic formulation)
  Wait (delay) 4 seconds for simulation to initialize properly
  Simulate for robot’s one complete traversal around the circle (kinematic formulation)
Square
  Move robot in square with specified constant twist command
  Side length of square specified as a constant parameter (0.5 m) in script
  Wait (delay) 4 seconds for simulation to initialize properly
  Simulate for robot’s one complete traversal around the square (kinematic formulation)
Speed variation hypothesis: as speed increases, trajectory profile will deviate further from ideal

## Slide 3: Implementation
Robot | launch robot from turtlebot3_bringup package
Circle | argument defaults: lin_vel = 0.1, ang_vel = 0.1
  Launch circle_node from assignment_1c package
  Launch rviz2 from rviz2 package and load configuration file from assignment_1c package
Square | argument defaults: lin_vel = 0.1, ang_vel = 0.1
  Launch square_node from assignment_1c package
  Launch rviz2 from rviz2 package and load configuration file from assignment_1c package
Move | argument defaults: maneuver = circle, lin_vel = 0.1, ang_vel = 0.1
  Launch circle_node or square_node from assignment_1c package depending on maneuver argument
  Launch rviz2 from rviz2 package and load configuration file from assignment_1c package

## Slide 4: Dependencies
TurtleBot3 Burger Robot Hardware with TurtleBot3 SBC Image
ROS2 Foxy Fitzroy on Ubuntu 20.04 Focal Fossa
TurtleBot3 Packages - Included with the assignment repository
TurtleBot3 Simulations Packages - Included with the assignment repository
TurtleBot3 Messages Package - Included with the assignment repository
TurtleBot3 Dynamixel SDK Packages - Included with the assignment repository
Source: ROS2 GitHub
Source: ROS2 Docs
Source: Ubuntu
Source: GazeboSim
Source: ROBOTIS Inc.

## Slide 5: Build Instructions
Make a directory ROS2_WS to act as your ROS2 workspace.
Clone the assignment repository.
Move assignment_1c directory to src of your ROS2_WS.
[Optional] Remove the unnecessary files.
Build the packages.
Source the setup.bash file of your ROS2_WS.
NOTE: Detailed instructions are available
in README.md file of the assignment repository.
Source: Tinker Twins GitHub

## Slide 6: Execution Instructions
Robot
  Launch robot.launch.py file from turtlebot_bringup package
Circle
  Launch circle.launch.py file from assignment_1c package
  Provide arguments for lin_vel and ang_vel (float)
Square
  Launch square.launch.py file from assignment_1c package
  Provide arguments for lin_vel and ang_vel (float)
Move
  Launch move.launch.py file from assignment_1c package
  Provide argument for maneuver (string)
  Provide arguments for lin_vel and ang_vel (float)
Source: Tinker Twins GitHub
NOTE: Detailed instructions are available in README.md file of the assignment repository.

## Slide 7: Results - Circle
Robot
RViz
Slow
Medium
Fast

## Slide 8: Results - Square
Robot
RViz
Slow
Medium
Fast

## Slide 9: Analysis
Parameter/Metric | Slow Circle | Slow Square | Medium Circle | Medium Square | Fast Circle | Fast Square
Resemblance to ideal trajectory | Very High | Low | High | Medium | Medium | Extremely Low
Kinematic behavior | Very High | High | High | Medium | Medium | Very Low
Time for 1 complete traversal | High | Very High | Medium | Medium | Very Low | Low
Note 1: The analysis presented above is qualitative.
Although a detailed quantitative analysis can be accomplished, it was beyond the scope of this assignment.
Source: Tinker Twins GitHub
Note 2: Deployment videos as well as pictures are available in README.md file as well as in the media directory of the
assignment repository.

## Slide 10: Thank You!