## Slide 1: AuE-8230 Autonomy: Science and Systems
Group 1: Chinmay Samak, Tanmay Samak
Capstone Project
Codebase

## Slide 2: Task 1
Wall Following

## Slide 3: Approach
Sensors: LIDAR
Algorithm:
  Front laser scan ranging measurement [0]
  Left [75:105] and right [255:285] laser scan sectors
  De-coupled lat-lon PID controller architecture
  Adaptive cruise control based on frontal range
  Cross-track error based on mean of left and right sectors
  Safety (inf range, actuation limits)
Alternate approaches:
  Different FOV and orientation of laser scan sectors
  CTE based on min, max, mean, wt. mean of sectors

## Slide 4: Approach
Sensors: LIDAR
Algorithm:
  Front laser scan ranging measurement [0]
  Left [75:105] and right [255:285] laser scan sectors
  De-coupled lat-lon PID controller architecture
  Adaptive cruise control based on frontal range
  Cross-track error based on mean of left and right sectors
  Safety (inf range, actuation limits)
Alternate approaches:
  Different FOV and orientation of laser scan sectors
  CTE based on min, max, mean, wt. mean of sectors

## Slide 5: Approach
Sensors: LIDAR
Algorithm:
  Front laser scan ranging measurement [0]
  Left [75:105] and right [255:285] laser scan sectors
  De-coupled lat-lon PID controller architecture
  Adaptive cruise control based on frontal range
  Cross-track error based on mean of left and right sectors
  Safety (inf range, actuation limits)
Alternate approaches:
  Different FOV and orientation of laser scan sectors
  CTE based on min, max, mean, wt. mean of sectors
Yes
Yes
Publish CMD_VEL =
{LIN_VEL, ANG_VEL}
Left Sector Mean
Right Sector Mean
CTE = LSM - RSM
CTE is
-inf?
Front Scan Range
LIN_VEL =
PID_LON(FSR)
Bound LIN_VEL
ANG_VEL =
-0.1 rad/s
ANG_VEL =
0.1 rad/s
CTE is
inf?
No
No
Initialize
START
Subscribe Laser Scan
Bound ANG_VEL
ANG_VEL =
PID_LAT(CTE)
END

## Slide 6: Results
Simulation
TurtleBot3
Remote PC

## Slide 7: Thank you!
…open to questions and suggestions