## Slide 1: AuE-8230 Autonomy: Science and Systems
Group 1: Chinmay Samak, Tanmay Samak
Capstone Project
Codebase

## Slide 2: Task 3
Line Following

## Slide 3: Approach
Sensors: Camera (compressed/uncompressed | 320x240 px)
Algorithm:
  Crop incoming image:
  Convert from RGB to HSV color space and mask specific color
  Calculate weighted average of pixel intensities (detect clusters)
  Calculate centroid of cluster and thereby deviation from line
  Constant lin_vel with PID controller for ang_vel
  Safety mechanisms and bounds (actuation limits)
Alternate approaches:
  Different ROI and HSV thresholds
  Tilting camera – tight curves

## Slide 4: Approach
Sensors: Camera (compressed/uncompressed | 320x240 px)
Algorithm:
  Crop incoming image:
  Convert from RGB to HSV color space and mask specific color
  Calculate weighted average of pixel intensities (detect clusters)
  Calculate centroid of cluster and thereby deviation from line
  Constant lin_vel with PID controller for ang_vel
  Safety mechanisms and bounds (actuation limits)
Alternate approaches:
  Different ROI and HSV thresholds
  Tilting camera – tight curves

## Slide 5: Approach
Sensors: Camera (compressed/uncompressed | 320x240 px)
Algorithm:
  Crop incoming image:
  Convert from RGB to HSV color space and mask specific color
  Calculate weighted average of pixel intensities (detect clusters)
  Calculate centroid of cluster and thereby deviation from line
  Constant lin_vel with PID controller for ang_vel
  Safety mechanisms and bounds (actuation limits)
Alternate approaches:
  Different ROI and HSV thresholds
  Tilting camera – tight curves
Publish CMD_VEL =
{LIN_VEL, ANG_VEL}
Initialize
START
Subscribe Image
END
Bound LIN_VEL and ANG_VEL
c_x, c_y = m10/m00, m01/m00
Cluster detected?
c_x, c_y = w/2, h/2
Crop Image
Convert from RGB to HSV
Compute moments
Apply HSV Thresholds
CTE = (w/2 - c_x + 10)/175
LIN_VEL = 0.05 m/s
ANG_VEL = PID_LAT(CTE)
Yes
No

## Slide 6: Results
Simulation
TurtleBot3
Remote PC

## Slide 7: Thank you!
…open to questions and suggestions