## Slide 1: AuE-8230 Autonomy: Science and Systems
Group 1: Chinmay Samak, Tanmay Samak
Capstone Project
Review Presentation 3

## Slide 2: Project Tasks
Task 1: Wall Following
Task 2: Obstacle Avoidance
Task 3: Line Following
Task 4: Stop Sign Detection
Task 5: AprilTag Tracking

## Slide 3: Project Timeline
Task 1: Wall Following
Task 2: Obstacle Avoidance
Task 3: Line Following
Task 4: Stop Sign Detection
Task 5: AprilTag Tracking

## Slide 4: Task 3
Line Following

## Slide 5: Primary Responsibility Assignment
Algorithm development: Tanmay
Simulation setup: Chinmay
Simulation deployment: Chinmay
Real-world deployment: Tanmay
Git repository management: Chinmay
Documentation: Tanmay
Note: Responsibility does not indicate contribution. Both members contributed equally to this project and have no conflict of interest to declare.

## Slide 6: Approach
Framework: ROS 2
Robot: TurtleBot3
Sensors: Camera (compressed/uncompressed | 320x240 px)
Algorithm:
  Crop incoming image:
  Convert from RGB to HSV color space and mask specific color
  Calculate weighted average of pixel intensities (detect clusters)
  Calculate centroid of cluster and thereby deviation from line
  Constant lin_vel with PID controller for ang_vel
  Safety mechanisms and bounds (actuation limits)
Codebase: GitHub

## Slide 7: Simulation Results

## Slide 8: Real-World Results
Robot
Remote PC

## Slide 9: Progress and Next Steps
Task 1: Wall Following
Task 2: Obstacle Avoidance
Task 3: Line Following
Task 4: Stop Sign Detection
Task 5: AprilTag Tracking
Calibration and optimization for final demo

## Slide 10: Challenges Faced
ROS 2 TurtleBot3 URDF size
ROS 2 DDS communication framework
  Domain ID not robust to network traffic fluctuations
  Topics not discoverable over network
  Conflicting QoS profiles for sensors and actuators
Unavailable ROS 2 packages and lack of resources
Gazebo world and texture setup for ROS 2
Gazebo residual errors and crashes

## Slide 11: Thank you!
…open to questions and suggestions